# NAVSO P-3641: Navy Power Supply Reliability Design & Mfg Guidelines

## Design Derating

4.2 Design for Reliability
Design Derating

The failure rate increases as a function of the applied stresses imposed by the initial design decisions. Depending upon the specific component type, construction and materials used, these failure-prone stresses may include voltage, current, or power dissipation. However, predominant among all others is temperature (case hot-spot, junction temperature, ambient temperature). Derating is simply the practice of designing equipment using components whose allowable maximum application stresses are constrained to some percentage of the Absolute Maximum Rating (AMR), thus taking advantage of the lower failure rate which results.

Absolute Maximum Rating

AMRs on parameters are derived by component manufacturers as guidance for designers in determining whether their component applications are compatible with anticipated worst-case stress conditions in their equipment. An AMR is usually based on one of the following:

(1) The stress point beyond which device performance parameters are not specified or controlled.

(2) The stress limit beyond which permanent degradation of parameters may begin to occur.

Voltage and Power Derating

Operating voltages and power dissipation levels are derated, for particular applications, to ensure that the components will operate at the required reliability levels under specified environmental conditions. Voltage and power derating are separate and independent procedures. Voltage derating is done to reduce the possibility of electrical breakdown, whereas power derating is done to maintain the component material below a specified maximum temperature.

The first step in the process of derating is to establish the operating voltages and the second step is to adjust the power dissipation level. The voltage derating of passive components prevents voltage breakdown, flashover and corona effects at the atmospheric pressure (altitude) to which the components are exposed. These effects are dependent upon voltage gradients, configuration of terminals and the nature of the dielectric path. The operating voltage of active components, such as semiconductors, is dependent upon the breakdown characteristics of the semiconductor material.

After the operating voltages are established, the power dissipation level is determined. The degree of heat transfer from a heat-producing component and the immediate ambient temperature surrounding the component, will determine the surface temperature or junction temperature, core temperature and hot-spot temperatures at a particular power level. The junction temperature should not exceed +110ºC under worst-case conditions.

Table 4-1 defines the minimum derating criteria that are recommended for the design of power supplies. TE000-AB-GTP-010 and NAVAIR AS-4613 may in some instances require more stringent derating. Each application should be considered individually whenever design penalties result. The parameters of the values listed under "DERATED TO % RATING" are shown in "DERATING PARAMETER."

# NAVSO P-3641: Navy Power Supply Reliability Design & Mfg Guidelines

TABLE 4-1. COMPONENT DERATING CRITERIA (Sheet 1 of 3)

| DERATED TO % RATING COMPONENT TYPE DERATING (Or Absolute Value PARAMETER Indicated) (See Note 1) |
| --- |
| RESISTORS Carbon Composition Film Hi Stability Wirewound Accurate Wirewound Power Wirewound Chassis Mounting Variable Wirewound Variable Nonwirewound Thermistor Tantalum Nitride Chip | Power/Voltage Power/Voltage Power/Voltage Power/Voltage Power/Voltage Power/Voltage Power/Voltage Power/Voltage Power/Voltage | 50/80 50/80 50/80 50/80 50/80 50/80 50/80 50/80 50/80 |
| CAPACITORS All Types All Types All Types Ceramic Glass Mica Film Dielectric Tantalum Solid Tantalum Wet {MIL-C-39005/22./25 only} Tantalum Foil Aluminum Electrolytic | Ripple Voltage Ripple Current Core Tempature Voltage Voltage Voltage Voltage Voltage Voltage Voltage Voltage | 50 70 20蚓 less than rated 50 50 60 dipped 40 molded 50 50 (Special 100% current surge test) 60 50 70 (Resin end seal protected and 99.96% aluminum foil purity) |
| RELAYS AM | Use Arc Suppression Contact Current (Continuous) Contact Current (Surge) Coil Energize Voltage Coil Dropout Voltage Vibration Contact Gap | 50 Resistive 25 Inductive 80 Hold to Manufacturer's Nominal Rating 75 (Including "0" of mounting) 0.005 minumum opening |
| Note 1: Passive high-voltage components have both volatge and electric field limitations. Refer to Section 5 for further guidelines. |

TABLE 4-1. COMPONENT DERATING CRITERIA (Sheet 2 of 3)

| DERATED TO % RATING COMPONENT TYPE DERATING (Or Absolute Value PARAMETER Indicated) (See Note 1) |
| --- |
| SWITCHES | Contact Current Voltage | 30 50 |
| CONNECTORS | Contact Current Voltage {Dielectric Withstanding} | 50 25 |
| MAGNETIC DEVICES {MIL-T-27} | Current (Continuous) Current (Surge) Voltage (Continuous) Voltage (Surge) Hot-Spot Temperature Insulation Breakdown Voltage Temperature Rise | 60 90 60 90 30°C below Insulation rating 25 40°C maximum |
| RF COILS | Current | 50 |
| TRANSISTORS | Power (See Note 2) Forward Current {Continuous} Voltage (See Note 3) Transient Peak Voltage Reverse Junction Voltage Junction Temperature | 50 60 75 75 65 110°C |
| Note 1: Passive high-voltage components have both volatge and electric field limitations. Refer to Section 5 for further guidelines. Note 2: The Safe Operating Area (SOA) curves, adjusted for junction temperature, shall not be exceeded under any transiant condition. Note 3: Power devices exhibiting "punch-through" characteristics should be derated to 50% on voltage parameters. |

TABLE 4-1. COMPONENT DERATING CRITERIA (Sheet 3 of 3)

| DERATED TO % RATING COMPONENT TYPE DERATING (Or Absolute Value PARAMETER Indicated) (See Note 1) |
| --- |
| DIODES Switching, General Purpose, Rectifier Zener SCR All | Current (Surge) Current (Continuous) Peak Inverse Voltage Current (Surge) Current (Continuous) Power Current (Surge) Current (Continuous) Peak Inverse Voltage Junction Temperature | 70 70 65 70 60 50 70 70 65 110蚓 maximum |
| MICROCIRCUITS Linear | Current (Continuous) Current (Surge) Voltage (Signal) Voltage (Surge) Voltage Reverse Junction (Signal) Voltage Reverse Junction (Surge) Junction Temperature Supply Voltage Junction Tempurature Fanout | 70 60 75 80 65 85 110蚓 maximum Hold to Manufacturer's Nominal Rating 110蚓 maximum 80 |
| Note 1: Passive high-voltage components have both volatge and electric field limitations. Refer to Section 5 for further guidelines. Note 2: Many families of digital microcircuits exhibit additional characteristics that may require derating (e.g., toggle frequency, hold times). The designer must use good engineering judgement to provide a conservative design (derating of parameters that could drift out of tolerance or cause premature aging or failure). |